## Slide 1: WEEK 06 Data Standardization lecture
Instructor: Yanan Wu
fALL 2025

## Slide 2: 6.1 Attribute table

## Slide 3
Cartography
  What is Cartography?
  What is map?
Data Standardization
  Density
  Proportion
  Relationship
  Statistic summaries
Data Classification
  Equal interval
  Quantiles
  Natural breaks
  Standard deviation
Overview

## Slide 4
Many different definitions, but only one ‘official’ definition for this course
  The art, science, and technology of making maps, together with their study as scientific documents and works of art - by International Cartographic Association
What is Cartography?

## Slide 5
These terms are all used to describe the process of making maps. However, they are not synonymous with Cartography.
  GIS
    A computer-based system for collecting, managing, analyzing, modeling, and presenting geographic data for a wide range of application
  Visualization has no agreed-upon definition.
    The representation of data in a viewable medium or format – by ESRI
    Include a reference to computer technologies and interactive maps
  Mapmaking
    Creating maps by any method
GIS, Visualization, and Mapmaking

## Slide 6
Many different definitions, but only one ‘official’ definition for this course
  A map is a reduced, selective, and symbolized graphical representation of the environment
    Reduced: we reduce the size of the spatial phenomenon being represented onto a more reasonably sized piece of paper.
    Selective: The maps should only include items that are directly related to the message of the map.
    Symbolized: The item being mapped by using a representative symbol.
What’s a Map?
Notes: It is reduced because it is physically smaller than the size of the United States.
It is selective because it does not show the relevant information to the purpose of this map.
It is symbolized through the use of visual variables such as color, texture, size, and shape.

## Slide 7
General-reference maps – United States
  It is reduced, selective, symbolized
What is a Map?
General Reference Map United States

## Slide 8
What is a Map?
General-reference maps – Atlanta Area
  It is reduced, selective, symbolized

## Slide 9
Special-purpose maps
  Large scale (showing a small area and much detail)
  Canal maps
What is a Map?

## Slide 10
Thematic maps
  Represent a single topic or theme (a single attribute or variable)
  Include only features that are directly related to the theme, or useful as reference
  Represent fewer features, in more depth
What is a Map?

## Slide 11
Credit: Cary Anderson© Penn State is licensed under CC BY-NC-SA 4.0(link is external). Data Sources: Esri, US Census Bureau
A county-level map of unemployment.

## Slide 12
Standardization
Normalization
Transformation of raw data values to different, more meaningful values
  To map densities instead of ‘raw’ values
  To map proportions between variables
  To map other relationships between variables
  To map statistic summaries

## Slide 13
Mapping Density
How much of a particular thing exists within a given area
Mapping density is not necessary if the goal is to show where ‘more’ is
  Larger enumeration units often have ‘more’ of a particular thing
  Accounting for the varying sizes of enumeration units can be more revealing
Notes: Enumeration Unit: An areal unit by which enumerated data is aggregated and quantified. A common example of enumeration units is areal census units. Census data is aggregated into enumeration units that include blocks, block groups, census tracts, zip codes, and metropolitan areas, among many others.
Large areas can be perceived as ‘more important' and small areas as less

## Slide 14
Population/Area
“Persons per Square Miles”
Population, 2010
Population Density, 2010
Mapping Density
National Geospatial Technology Center of Excellence
Notes: contiguous
Connecticut

## Slide 15: Choosing the Right Visual Type
Raw values
Counts
Totals
Color
Derived values
Percentages
Averages
Rates
Ratios
Color
  b. Spatial Data – Choropleth Map

## Slide 16
Bushels/Area
“Bushels per Acre”
Mapping Density
National Geospatial Technology Center of Excellence

## Slide 17
Mapping Proportions
Proportions represent the relationship of a part to a whole
Several ways to express proportions
  Quotient: 0.0 - 1.0
  Percentage: 0 - 100%
  Rate: 7 per 1,000

## Slide 18
Persons 60 and Over/Total Persons*100
“Percentage of Seniors”
Persons 60 and Over
Mapping Proportions
National Geospatial Technology Center of Excellence
Notes: Spain, Population ageing
28.7 % in Japan

## Slide 19
Non Grads/Total Population*100
“Percentage of non Grads”
Mapping Proportions
National Geospatial Technology Center of Excellence

## Slide 20
It can be revealing to show how two variables are related (in a manner that is not strictly proportional)
Several ways to express proportions
  Quotient: 0.0 - infinity
  Percentage: 0 - infinity%
  Rate: 1,500 per 100
Mapping Relationships

## Slide 21
Mapping Relationships
  Rate: Men per 100 women

## Slide 22
Acres of Cropland/Population
“Acres per 1,000 People”
Mapping Relationships
National Geospatial Technology Center of Excellence
Notes: Intergovernmental Panel on Climate Change
Vatican

## Slide 23
Mapping Stat Summaries
Enumeration units can be represented according to calculated statistics
  Median
  Mean (average)
  Standard Deviation, etc.

## Slide 24
Average Household Size, 2020
Mapping Stat Summaries
https://uca-gis.maps.arcgis.com/home/webmap/viewer.html?webmap=36d7e68ce0ab416d951300479fc6fc04

## Slide 25
Transformation of raw data values to different, more meaningful values
  Densities, proportions, relationships, and statistical summaries
  In conjunction with data classification, data standardization allows us to craft our message

## Slide 26: Interactive Vote Map(Web) from New York Times
What type of map is it?
What color scheme does it use?
Notes: This is primarily a Choropleth Map. It uses colored geographic areas (counties, or possibly even smaller precincts given the title "Extremely Detailed") to represent the intensity or proportion of a variable – in this case, the 2020 US Presidential election results.
The map uses a Diverging Color Scheme. t employs two distinct hues: Red (typically representing the Republican candidate, Donald Trump) and Blue (typically representing the Democratic candidate, Joseph Biden).
The design uses a main map display area accompanied by a distinct left-hand sidebar. This is a common layout for interactive web maps. A clear legend is positioned unobtrusively in the bottom left corner.
The map utilizes interactive annotations (tooltips/pop-ups). Static labels for major features like state names are included directly on the map in a subtle color and font size, providing geographic orientation without dominating the visualization.

## Slide 27: Hurricane Milton Strength Timeline, 10/5/2024 – 10/10/2024
Progression of Hurricane Milton's shape and intensity
Inset map: Temperature
Points: Wind speed and category along its path at specific times.

## Slide 28: 4.3 Resources for Good Maps
ESRI MAP GALLERY
QGIS MAP GALLERY
David Rumsey Map Collection
The historical map collection has over 139,000 maps and related images online.

## Slide 29: 4.4 Resources for Bad Maps
Examples of Bad Maps
Examples of Bad Maps

## Slide 30
Thank you!