## Slide 1: Lecture 07 Digitizing, Georeferencing, Resampling lecture
Instructor: Yanan Wu
fALL 2025

## Slide 2: 7.1 MAP ELEMENTS

## Slide 3
Digitizing
  Digitizing types
  Digitizing steps
  Snapping
  Georeferencing
  Control points
  Transformation methods
  Resampling
  Resampling methods
Overview

## Slide 4
Digitizing
The process by which coordinates from a map, image, or other sources are converted into a vector layer in a GIS.
Notes: The x, y coordinates of these features are automatically recorded and stored as spatial data.

## Slide 5
Digitizing
Manual digitization is human-guided coordinate capture from a map or image source.
  On-screen digitizing
    Heads-up digitizing, involves manually digitizing on a computer screen, using a digital image as a backdrop
Bolstad, 2019
Notes: The x, y coordinates of these features are automatically recorded and stored as spatial data.

## Slide 6
Digitizing
Manual digitization is human-guided coordinate capture from a map or image source.
  Hardcopy digitizing
    Human-guided coordinate capture from a paper, plastic, or other hardcopy map
Bolstad, 2019
Notes: electrically sensitized puck. The most common digitizers are based on a wire grid embedded in or under a table

## Slide 7
Digitizing
Manual digitization is human-guided coordinate capture from a map or image source.
  Scan digitizing

## Slide 8
Obtain input imagery or other reference data
Create a new file to edit into
  Define geometry (point, lines, or polygon)
  Define projection
  Create attribute fields
Digitizing
Edit attribute information
Check and validate your results
Digitizing Steps
Notes: Before beginning to digitize, you will need to obtain some input imagery or other reference data.
You will then need to create a new shapefile or feature class to draw into. This will require defining the geometry (point, line, or polygon), setting the projection or coordinate reference system, and creating any required attribute fields.
You can then draw the new features using the reference data. You will also need to edit the attribute table.
It is always important to validate your results for quality control purposes.

## Slide 9
Use Edit tab
Remember to consider topology
Remember to edit attributes
Save often!!!!!!!
Digitizing in ArcGIS Pro
Notes: Digitizing options are available in the Edit Tab.
As you edit the geometry and attributes, remember to save often so you don’t lose any work.

## Slide 10
Make sure to define the correct type
Data Type | 
Short Integer | Integer values between -32,768 and 32,767
Long Integer | Integer values between -2,147,483,648 and 2,147,483,647
Float | Decimal values with 1-6 decimal places
Double | Decimal values with more the 6 decimal places
Text | Text strings
Date | Data info (mm/dd/yyyy)
Adding Fields
Notes: When creating a new field, you will need to define the field type.
Short and long integer fields can only store integer or whole number values. Long integers can stored a wider range of numbers than short integers.
If you need to maintain decimal values, you cannot use a short or long integer. Instead, you must use a float or double type. Float fields can store up to 6 decimal places while double can store more than 6.
If you would like to store text or string data, you will do so in a text field. Note that numbers stored in text field will be treated like strings. They will not be treated line numbers. For example, you will not be able to perform mathematical operations on these data.
Date fields store dates and will treat the information as dates.

## Slide 11
Use Add/Calculate Geometry Attributes Tool
Points | Lines | Polygons
X-coordinate | Start-X | Area
Y-coordinate | Start-Y | Perimeter
Z-coordinate (if z-enabled) | End-X | Centroid-X
M-coordinate (if m-enabled) | End-Y | Centroid-Y
 | Mid-X | 
 | Mid-Y | 
 | Length | 
 | Bearing | 
Adding Geometric Fields
Notes: Different geometric measures can be calculated and stored in the attribute table for points, lines, and polygon data.
For point data, it is possible to store the x and y coordinate. If the feature is Z-enabled, or contains elevation or height information, this value can also be calculated. If it is M-enable, the M coordinate can be calculated. M-coordinates generally relate to positions along a network.
For lines, you can calculate the x and y coordinates for the start, end, and middle of the line segment. You can also calculate the length and bearing. The bearing is the compass direction of the line and is defined as the direction of travel from the start to the end node.
For polygons, you can calculate the area and perimeter. The perimeter is the length of all the lines that make up the polygon. You can also calculate the centroid, or geometric center, coordinates. Note that centroid coordinates can sometimes be misleading. For example, for irregular or elongated shapes, the centroid may not actually occur within the polygon. For a “C” shaped feature, the centroid would occur somewhere in the middle of the “C” as oppose to within the area that makes it up. So, be careful when using centroid measures.

## Slide 12
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Source data errors
Bolstad, 2019
The surface error caused by 1 millimeter digitizing error

## Slide 13
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Precision of equipment
  The abilities and attitude of the person digitizing affects the geometric quality of manually digitized data
Bolstad, 2019
Notes: Dangling include overshoot and undershoot, and two lines with points not connected. Dangling node include undershoot and overshoot node.

## Slide 14
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Precision of equipment
  The abilities and attitude of the person digitizing affects the geometric quality of manually digitized data
      Topology
Bolstad, 2019

## Slide 15
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Precision of equipment
  The abilities and attitude of the person digitizing affects the geometric quality of manually digitized data
      Snapping
Bolstad, 2019

## Slide 16
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Precision of equipment
  The abilities and attitude of the person digitizing affects the geometric quality of manually digitized data
      Reshaping

## Slide 17
Impacts on Digitizing Accuracy/ Precision
Factors affect accuracy of digitizing
  Precision of equipment
  The abilities and attitude of the person digitizing affects the geometric quality of manually digitized data
  Common feature inconsistency
    Using a master boundary
Bolstad, 2019

## Slide 18
Group Activity
Identify a characteristic feature or error in digitizing at each of the labeled letter locations in the drawing below.
Bolstad, 2019
Notes: a-undershoot; b-undershoot; c-psuedonode; d-overshoot; e-undershoot; f-missing label; g-overshoot.

## Slide 19
Process of aligning an unreferenced dataset with one that has spatial reference information.
Georeferencing
Bolstad, 2019
Notes: Georeferencing is the process of aligning an unreferenced dataset with one that has spatial reference information.
As an example, you may want to use a paper map in your GIS. In order to use it effectively with other data layers, it will need to be referenced to the correct location in the map space. So, you will need to create a digital data file then apply a process to align it to other data layers in the map space. This is the process of georeferencing.
When aerial or satellite imagery are collected, they also need to be referenced to the correct location in the map space.
So, this is a common preparatory task when working with spatial data.
Many GIS and remote sensing software packages provide georeferencing tools.

## Slide 20
Convert paper map to digital raster data
Resolution and quality depends on the quality of original paper data and scanning settings (e.g., dots per inch (dpi))
Can be converted back to vector data via digitizing or tracing
Scanning
Notes: The quality of the scanned raster image will partially depend on the quality of the analog data. However, the scanning settings can also have an impact, such as the dpi used.
Make sure that you use adequate settings to scan in quality data.
Once data have been scanned in and georeferenced, vector data can be generated by digitizing or tracing over the map data.

## Slide 21
Used to register dataset to known location
Used as reference and represent the same location in the data being referenced and reference data
Control Points
Bolstad, 2019
Notes: Control points are an important component of the georeferencing process.
Control points are used as reference and represent the same location in the data being referenced and reference data.
Control points can be created by digitizing examples on the screen.
Whenever aerial imagery is collected, it is common for ground control points to be placed on the ground prior to the data collection. These ground targets are surveyed using GPS equipment. An analyst can then use the ground targets in the image and their associated coordinates to georeference the data. This method generally produces quality results. However, this is only possible if control points can be placed in the image prior to the data collection.
So, many times were are forced to create control points on the computer screen and georeference our data relative to a dataset that has already been referenced, such as aerial imagery.

## Slide 22
Used to register dataset to known location
Used as reference and represent the same location in the data being referenced and reference data
Control Points
Notes: Control points are an important component of the georeferencing process.
Control points are used as reference and represent the same location in the data being referenced and reference data.
Control points can be created by digitizing examples on the screen.
Whenever aerial imagery is collected, it is common for ground control points to be placed on the ground prior to the data collection. These ground targets are surveyed using GPS equipment. An analyst can then use the ground targets in the image and their associated coordinates to georeference the data. This method generally produces quality results. However, this is only possible if control points can be placed in the image prior to the data collection.
So, many times were are forced to create control points on the computer screen and georeference our data relative to a dataset that has already been referenced, such as aerial imagery.

## Slide 23
Used to register dataset to known location
Used as reference and represent the same location in the data being referenced in reference data
Control Points
Notes: Control points are an important component of the georeferencing process.
Control points are used as reference and represent the same location in the data being referenced and reference data.
Control points can be created by digitizing examples on the screen.
Whenever aerial imagery is collected, it is common for ground control points to be placed on the ground prior to the data collection. These ground targets are surveyed using GPS equipment. An analyst can then use the ground targets in the image and their associated coordinates to georeference the data. This method generally produces quality results. However, this is only possible if control points can be placed in the image prior to the data collection.
So, many times were are forced to create control points on the computer screen and georeference our data relative to a dataset that has already been referenced, such as aerial imagery.

## Slide 24
Criteria for control points:
  Spread evenly around study area
  Enough points to use the algorithm of choice
  Use highest accuracy dataset possible
  Use locations identifiable on both datasets (known & unknown)
  From Point: location on the data being referenced
  To Point: same location on the reference data
Control Points
Notes: Collecting quality control points is key for successful georeferecning. Here are some suggestions for collecting quality control points.
First, the control points should be spread evenly around the study area. If the control points are only collected within the center of the image, the algorithm used will have a difficult time accurately referencing the margins of the image. So, make sure to include some points in the image margins.
You should have enough points to use the georeferecning algorithm of choice. The number of points needed depends on the algorithm, which we will discuss later.
Any positional errors in the input data will impact the georeferecning result. So, it is important to use quality reference data. Generally, we rely on high resolution imagery.
Locations must be identifiable in both datasets, the data being referenced and the reference imagery.
Generally, I try to obtain as many quality reference points as possible. However, adding more points that may be suboptimal can cause issues. So, make sure the points that you use can be accurately located in both images. Adding points that are of low quality can decrease the quality of the result.
When defining a control point, you will need to identify it in both datasets. The from point is the location on the data being referenced while the to point is the location relative to the reference data. The algorithm will attempt to move the from point location to the to point location.

## Slide 25
In order to georeferenced data, it may need to be:
  Translate
  Scale
  Rotate
  Skew
These transformations are applied mathematically.
Transforming the Data
Notes: When performing georeferencing different transformations can be applied.
Translation implies moving the image without changing its shape or size.
Changing the scale means to change the size of the image but not the shape.
Rotation will reorient the scene relative to a point of rotation.
Skew is used to change or distort the shape of the data.
The transformations that can be applied depends on the algorithm used.

## Slide 26
Zero-Order Polynomial = just translate the data (need 1 control point)
First-Order Polynomial (Affine) = translate, scale, and rotate (need 3 control points)
Higher Order = more complex distortions can be corrected
  Rarely use higher than third order
  Need more control points
  If raster dataset must be bent or curved, use a second- or third-order transformation
Transformation Method
Notes: Polynomial equations can be used for georeferencing.
Zero-order polynomials can only shift or translate the image and require only a single control point.
First-order polynomials can translate, scale, and rotate the data. However, they cannot change the shape or skew the image. Three control points are required.
Higher order polynomials can apply all four distortions and require more than three control points. We rarely use higher than third order polynomials for georeferencing.

## Slide 27: First-Order Polynomial (Affine)
X = Ax + By + C
Y = Dx + Ey + F
X = new x coordinate
Y = new y coordinate
x = original x coordinate y = original y coordinate
Image Row #
(Map) Northings (m)
x
x
x
x
x
Example by Dr. Tim Warner
Transformation Method
Notes: This slide provides an example of a first-order polynomial, also called an affine transformation.
Here, the new X and Y coordinates are predicted using the original x, and y coordinates. Note that both coordinates are used to predict each of the new coordinates.
The goal here is to determine appropriate coefficients to transform the data. Note that x and y are not raised to a power, as this in only first-order, so no square or cubed terms can be used.
The A term and D terms relate to changing the scale in the x and y directions, respectively. The B and E terms relate to rotation, and the C and F terms relate to translation. Again, this method does not allow for a skew to be applied.
The terms are determined using the control points.

## Slide 28
Adjust = combines polynomial and triangular irregular network (need 3 control point)
Similarity = first order transformation which tries to preserve the shape of the original raster (need 3 control points)
Projective = commonly used for image data (need 4 control points)
Spline = uses rubber sheeting (need 10 control points)
Transformation Method
Notes: Other methods are available that do not rely on or solely rely on polynomial equations. This slide provides some examples.
Again, different projection methods require different numbers of control points.
The optimal method will depend on the data being referenced, the control points used, and the required transformations.

## Slide 29
Root mean square error (RMSE)
Measure of how well the now-referenced data matches with the source
Obtained by comparing the known location of the control point with the computed coordinates of the control point.
RMSEx = √ Σ(xpredicted – xactual)2/n
RMSEy = √ Σ(ypredicted – yactual)2/n
RMSE = √ (RMSEx2 + RMSEy2)
Assess the quality of georeferenced result
Bolstad, 2019
Notes: Georeferencing is generally assessed using the root mean square error, or RMSE, statistic.
This measure provides an assessment of how well the now referenced data matches the source or reference image.
It is generally calculated by comparing the known location of the control point with the computed coordinates of the control point.
The predicted x and y coordinates are subtracted from the correct location to obtain a residual or error. The residuals are then squared, summed, then divided by the number of samples. Lastly the square root is taken. This will provide a RMSE for the x and y directions. These measures can then be combined to obtain a total RMSE.
RMSE will be reported in the map units or as number of pixels. Lower RMSE is better.

## Slide 30
Correct X | Correct Y | Predicted X | Predicted Y | X residual | Y residual | X residual squared | Y residual squared
513,126.80 | 4,101,294.60 | 513,127.30 | 4,101,293.40 | 0.5000 | -1.2000 | 0.2500 | 1.4400
513,123.20 | 4,101,303.40 | 513,118.10 | 4,101,302.10 | -5.1000 | -1.3000 | 26.0100 | 1.6900
513,203.80 | 4,101,209.10 | 513,203.10 | 4,101,207.20 | -0.7000 | -1.9000 | 0.4900 | 3.6100
513,182.60 | 4,101,377.80 | 513,181.60 | 4,101,379.90 | -1.0000 | 2.1000 | 1.0000 | 4.4100
513,217.60 | 4,101,403.60 | 513,216.10 | 4,101,405.20 | -1.5000 | 1.6000 | 2.2500 | 2.5600
 |  |  |  |  |  | RMSE X | 2.45
 |  |  |  |  |  | RMSE Y | 1.66
 |  |  |  |  |  | RMSE | 2.96
Assess the quality of georeferenced result
Notes: This slide provides an example of an RMSE calculation.
The correct and predicted x and y coordinates are differenced to obtain a residual. The residuals are then squared, summed, then divided by the number of samples. The last step is to take the square root.
Once the RMSE is obtained in the x and y directions, they can be combined to obtain a total RMSE.
In this example, the total RMSE is 2.96 meters. This suggest that each pixel is, on average, 2.96 meters from its correct location.
What is considered an acceptable RMSE? This depends on many factors. For example, coarser spatial resolution data will tend to have a larger RMSE than fine resolution data as the larger pixel or cell size will result in some spatial ambiguity.
For imagery, our goal is generally to obtain and RMSE that is smaller than the dimensions of a pixel or cell.
Some mapping tasks may require better georeferencing results than others. There will always be some georeferencing or positional error in your data.

## Slide 31
  Calculate RMSEx, RMSEy, and RMSE using Excel sheet
Individual Activity
Notes: Positional uncertainty relates to differences in the position of your data relative to the correct location.
You can consider uncertainty in 2D space as x and y coordinates in a geographic or projected space.
You can also consider the uncertainty of elevation measurements.
Combining these, you can consider uncertainty in 3D space.
As an example, the image shows some uncertainty in a vector line road dataset in comparison to the orthophotography.
Positional error is generally assessed using root mean square error or RMSE, similar to how georeferencing results are assessed.
All spatial data have some positional uncertainty; however, this is only a concern if there is too much uncertainty to support your analysis or mapping needs.

## Slide 32
The lower RMSE generally indicates a more accurate affine transformation
For imagery, we generally want the RMSE to be lower than the size of the pixel
Low RMSE can be misleading if the quality of the control points is poor
Sometimes the algorithm overfits to the control points, so the RMSE can be misleading
The RMSE is not useful when comparing among different model forms
RMSE Interpretation
Notes: Here are some other notes regarding interpreting RMSE.
Note that RMSE can be misleading if the quality of the control points is suspect or poor.
Also, algorithms commonly overfit to the control points. So, if control points are used to calculate RMSE, the accuracy can be inflated.
It is best to withhold data points and calculate RMSE relative to these locations.

## Slide 33
RMSE Interpretation
Bolstad, 2019
Notes: Here are some other notes regarding interpreting RMSE.
Note that RMSE can be misleading if the quality of the control points is suspect or poor.
Also, algorithms commonly overfit to the control points. So, if control points are used to calculate RMSE, the accuracy can be inflated.
It is best to withhold data points and calculate RMSE relative to these locations.

## Slide 34
Change the cell size
500 m cell size
Resampled 8,000 m cell size
Resampling
Notes: Resampling is used to change the cell size of raster data. Generally, cells are made larger, or the data are coarsened, since making the cells smaller will not really add information but will just duplicate existing values. You can’t increase the detail by simply resampling a coarser dataset to a finer resolution.
You may resample raster data to make it easier to process over large extents or to change the cell size to match other inputs in an analysis.
We will now talk about methods used to resample raster data.

## Slide 35
Majority Resampling
  Resamples using the most common cell value
  Good for categorical data
Resampling
Notes: Majority resampling will assign the most common cell value of the original cells that fall within the new cell to the new cell.
This method is not generally used for continuous data. It is more commonly used for categorical data.
For example, if a land cover categorical raster grid was resampled using this method, each new cell would be assigned the majority land cover class from the smaller original cells that fall inside of it.

## Slide 36
Nearest Neighbor
  New value will be the value of the original cell closest to the center of the new (larger) cell
  Good for categorical data
Resampling
Notes: Nearest neighbor resampling assigns the closest cell value from the original raster grid to the new cell.
No averaging is performed, so this method can be used to resample both categorical and continuous data.

## Slide 37
Bilinear Interpolation
Uses the inverse distance-weighted average of the four nearest pixel values to estimate a new pixel value
The four cell centers from the input raster that are closest to the cell center for the output processing cell will be weighted based on inverse distance and then averaged
Good for continuous data
Creates a smoothed surface
http://desktop.arcgis.com/en/arcmap/latest/extensions/spatial-analyst/performing-analysis/cell-size-and-resampling-in-analysis.htm
Resampling
Notes: Bilinear interpolation uses the inverse distance-weighted average of the four nearest pixel values in the original grid to estimate the new cell value.
The four cell centers from the input raster that are closest to the cell center for the output processing cell will be weighted based on inverse distance and then averaged. So, nearer cells will have a larger weight in the calculation than cells that are further away.
Since averaging is performed, this method is not appropriate for categorical data. However, it can be used for continuous data.
This method tends to smooth the image or raster data.

## Slide 38
Resampling
Bilinear Interpolation
Uses the inverse distance-weighted average of the four nearest pixel values to estimate a new pixel value
The four cell centers from the input raster that are closest to the cell center for the output processing cell will be weighted based on inverse distance and then averaged
Good for continuous data
Creates a smoothed surface
Notes: Bilinear interpolation uses the inverse distance-weighted average of the four nearest pixel values in the original grid to estimate the new cell value.
The four cell centers from the input raster that are closest to the cell center for the output processing cell will be weighted based on inverse distance and then averaged. So, nearer cells will have a larger weight in the calculation than cells that are further away.
Since averaging is performed, this method is not appropriate for categorical data. However, it can be used for continuous data.
This method tends to smooth the image or raster data.

## Slide 39
Cubic Convolution
Similar to bilinear interpolation, except the 16 nearest input cell centers and their values are used
Good for continuous data
http://desktop.arcgis.com/en/arcmap/latest/extensions/spatial-analyst/performing-analysis/cell-size-and-resampling-in-analysis.htm
Resampling
Notes: Cubic convolution is similar to bilinear interpolation except that the nearest 16 cells are used as opposed to the nearest 4. Since it makes use of averaging, it is also not appropriate for categorical data but can be used for continuous data.
This method tends to sharpen edges more than bilinear interpolation.
Bilinear interpolation and cubic convolution are both commonly used to resample image data.

## Slide 40
Pixel Aggregation
Generates a reduced-resolution version of a raster grid
Each output cell contains the Sum, Minimum, Maximum, Mean, or Median of the input cells that are encompassed by the extent of that cell
Resampling
Notes: Another option to change the cell size is to use pixel aggregation. This is also sometimes refered to as image degradation.
When using this method, a statistic from the cells that fall within the new larger cell is calculated and returned to the new cell.
Examples include sum, minimum, maximum, mean, or median.
The raster data can only be reduced in resolution in such a manner that a whole number of input cells will fall perfectly within a new cell. For example, a 2 by 2 meter raster grid could be converted to a 4 by 4 meter grid but not a 3 by 3 meter output.
This method can be used for both categorical and continuous data depending on the statistic returned.

## Slide 41
A good resource:
http://desktop.arcgis.com/en/arcmap/latest/extensions/spatial-analyst/performing-analysis/cell-size-and-resampling-in-analysis.htm
Resampling in ArcGIS Pro
Notes: If you would like to read more about resampling, check out this ESRI link.
Note that resampling is made available in a variety of GIS and remote sensing software packages.

## Slide 42
Thank you!