## Slide 1: GEOG 2475: Geographic Information Systems I
Yaqian He, PhD
Assistant Professor
Department of Geography
Lecture 07 Map Elements

## Slide 2
Map Elements
  Frame Line and Neat Line
  Mapped Area
  Inset
  Title and Subtitle
  Legend
  Data Source
  Scale
  Orientation
Overview

## Slide 3
The building blocks of Cartographic Communication
All maps are created from a common set of map elements
GeoTech
Map Elements

## Slide 4
Available Space
  Areas on a page or screen that can be used to place map elements
  “White Space”
The cartographer constantly evaluates the relationship between map elements and available space
  Map elements are usually visually centered within appropriate areas of available space
It is the cartographer’s job to make all decisions regarding map elements
  Which to include, and which to omit
  How to implement them in the most appropriate manner
Map Elements

## Slide 5
Map Elements
Which one is better?
Notes: A noisy, inefficient communicator
A simple, efficient communicator

## Slide 6
Frame Line and Neat Line
Mapped Area
Inset
Title and Subtitle
Legend
Data Source
Scale
Orientation
Decrease in size from top to bottom
Listed in the recommended order of placement: larger first, smaller last
Map Elements

## Slide 7
Alignment and centering of map features is a common task
Can be performed through “visual approximation”
  Features look properly aligned or centered
Can also be performed through precise measurement
  Features are exactly aligned or centered, using software controls
Alignment and Centering

## Slide 8
It is important to understand the terminology
  Horizontal and vertical are often confused
Horizontal
(Side-to-Side) Alignment and Centering
Vertical
(Top-to-Bottom) Alignment and Centering
Alignment and Centering

## Slide 9
Alignment and Centering
Inkscape
Illustrator

## Slide 10
Help to organize the map’s contents, and define its extent
Frame Line
  Encloses all other map elements
  Should be the first map element placed, because it occupies the most area, and defines the initial available space
Neat Line
  Is used to crop (limit the extent of) the mapped area
  Separate elements to provide an organized look
Frame Line
Neat Line
Frame line and neat line
GeoTech

## Slide 11
Help to organize the map’s contents, and define its extent
Frame Line
  Encloses all other map elements
  Should be the first map element placed, because it occupies the most area, and defines the initial available space
Neat Line
  Is used to crop (limit the extent of) the mapped area
  Separate elements to provide an organized look
Frame line and neat line
Peterson, 2021

## Slide 12
A Frame Line should be used in most situations
A Neat Line is used when the mapped area needs to be cropped or elements need to be separated
Frame line and neat line
GeoTech

## Slide 13
In certain cases, a frame line can also act as a neat line
  Enclosing all map elements and cropping the mapped area
Frame line and neat line
GeoTech

## Slide 14
The style of these lines should be subtle
  A single, thin, black line should be used in most cases
  Slightly thicker lines are appropriate when working with large wall maps
  These lines should focus attention on what is within them, not on themselves
Frame line and neat line

## Slide 15
Which one is better?
Discussion

## Slide 16
The region of Earth being represented
Consists of Thematic Symbols
  Thematic Symbols directly represent the map’s theme
  Are visually dominant
Can also include base Information
  Base Information provides a geographic frame of reference for the theme
  Is subdued
Mapped area

## Slide 17
Mapped area
Thematic Symbols: Shaded Polygons
Base Information:
Railroads and
City Label

## Slide 18
There are two varieties of mapped area, distinguished by how they represent the geographic region of interest
  Floating
  Cropped
Mapped area

## Slide 19
Floating Mapped Area
  Region of interest is disconnected from neighboring regions
  Produces available space that often eases the placement of other map elements
  Removes the region from its geographic context, possibly confusing the map user
Mapped area

## Slide 20
Cropped Mapped Area
  Represents the region of interest within its geographic context
  More realistic, less abstract
  Can make the placement of other map elements more difficult due to a lack of available space
Mapped area
Demonstration!
Iraq
Turkmenistan
Afghanistan
Notes: Iraq, Turkmenistan, Afghanistan, Pr

## Slide 21
Make the mapped area as large as possible within the available space
  Without being “too close” to the frame line
  While leaving ample room for the remaining map elements
Maximum area is important
  The mapped area—thematic symbols in particular—is instrumental in communicating the map’s information
Mapped area

## Slide 22
Try to visually center the mapped area both horizontally (side-to-side) and vertically (top-to-bottom)
    Within the available space, as defined by the frame line
This will not always result in an appropriate placement
    But should be tried first
Mapped area

## Slide 23
Appropriately Sized
Too Small
Too Large
Too Small and Off Center
Discussion

## Slide 24
A smaller map included within the context of a larger map
  Can serve several purposes
  In the world of ArcGIS, the inset is usually a separate data frame
Inset

## Slide 25: Features not in the correct geographic location
Inset

## Slide 26
Can be used to show the primary mapped area in relation to a larger, more recognizable area (a locator map)
Shows Relative Location
Inset

## Slide 27
Can be used to enlarge important or congested areas (a zoom, or blow-up map)
Shows Enlargement of an Area
Inset

## Slide 28
Can be used to show topics that are related to the map’s theme, or different dates of a common theme
Shows Related Themes or Dates
Inset

## Slide 29
The title and subtitle tell the map user what the map is about
Most thematic maps require a title
  A title is sometimes omitted when a map is used as a figure in a written document, assuming that the title is clearly expressed in the figure caption
  A well-crafted title can draw attention to a map
Title and Subtitle

## Slide 30
Title

## Slide 31
The Title of a thematic map is a succinct description of the map’s theme
  General reference maps typically employ the geographic region as the title
Unnecessary words should be omitted
  But avoid cryptic abbreviations
Appropriate Titles
Inappropriate Titles
Title
Notes: Don’t include the word “Map” in a title!

## Slide 32
The subtitle, if employed, is used to further explain title
  The geographic region and date are common components of the subtitle but is often omitted (when it is easily identifiable)
  The subtitle should be horizontally centered below the title
  The style of the Title and Subtitle should be plain
Title with Subtitle

## Slide 33
Title with Subtitle

## Slide 34
Use a subtle mask behind the title and subtitle only if it is necessary to cover the underlying mapped area to improve legibility
Title with Subtitle

## Slide 35
If possible, place the title at top-center,
The title should normally be the largest type on a thematic map – subtitle smaller
Both the title and subtitle should be short and to the point (limited to one line each)
Title with Subtitle

## Slide 36
Discussion

## Slide 37
Defines the symbols found on a map
  On a thematic map, thematic symbols are defined, in addition to symbols for base information that are not self-explanatory
  Legends for general reference maps often define all symbols found on the map—even if self-explanatory
Legend

## Slide 38
Legend

## Slide 39
The style of the legend should be clear and straightforward
  Use a subtle mask around the legend only if necessary to improve legibility
Symbols in the legend should be identical to those on the mapped area
  This includes color and orientation
Don’t include the word “Legend”!
Legend
Notes: size

## Slide 40
Representative symbols should be placed on the left and defined to the right
Symbols should be vertically centered with their definitions
Textual definitions and definitions consisting of individual numbers should be horizontally aligned to left
Legend

## Slide 41
Definitions containing numbers of 1,000 or greater should incorporate commas
Decimal numbers smaller than one should incorporate a leading zero
Legend

## Slide 42
The legend can be oriented horizontally
  Definitions are horizontally centered below the symbols they represent
  Symbols are vertically aligned to bottom
Legend

## Slide 43
Legend rectangles should be connected when representing the magnitude of an attribute
  Areal symbols on the mapped area are usually connected
  Connected rectangles help to emphasize the idea that a continuum of values is being represented
Legend
Inappropriate

## Slide 44
Areal symbols can be represented by irregular, amorphous polygons
  Irregular polygons can look more natural
  Most appropriate for qualitative categories of areal data (separated)
Appropriate
Legend

## Slide 45
A legend heading is often included to further explain the map’s theme
  The unit of measure (for quantitative data) and enumeration unit are common components of the legend heading
Legend

## Slide 46
The legend heading should be placed above the legend, and be horizontally centered with it
  Multiple lines of type can be horizontally centered (center justified)
  Horizontal centering creates a self-balancing group of objects
Legend
Appropriate
Inappropriate

## Slide 47
Legend symbols are often organized into groups, according to a certain logic
Legend

## Slide 48
The legend should be large enough to be useful
  But should not occupy vast areas of space, or challenge thematic symbols
Too Large
Too Small
Legend

## Slide 49
If possible, the legend should be visually centered within a larger portion of available space
Legend

## Slide 50
Discussion
Which one is better? And Why?

## Slide 51
Allows the map user to determine where data were obtained
  Sources of base information are normally omitted from thematic maps
Should be formatted similar to a standard bibliographic reference, but is often more concise and less formal
Data source

## Slide 52
The words “Data Source:” or “Source:” should be included to avoid ambiguity
  The data source indicates where data came from, not map authorship
A separate block of type can be used to indicate map authorship
The style of the data source should be plain and subtle
Publication names should be italicized
Multiple lines of type should be horizontally centered (center aligned)
Data source

## Slide 53
Data source

## Slide 54
The data source should be among the smallest type on a map
  Its purpose is to inform the curious, not to attract attention
Center it below the legend
  Or tuck it into a lower corner
Data source

## Slide 55
Indicates the amount of reduction that has taken place on a map, or allows the map user to measure distances
Can take three forms
  Representative Fraction (1:24,000)
  Verbal Scale (“One Inch to the Mile”)
  Bar Scale or Scale Bar
Scale
Notes: larger scale: greater detail and smaller area
Smaller scale: less detail and larger area

## Slide 56
Scale

## Slide 57
The bar scale is preferred format for inclusion on a thematic map
  Resembles a ruler
  Remains true when a map is enlarged or reduced (representative fractions and verbal scales don’t)
  Include if distance information can enhance the map user’s understanding of the theme
Scale
Notes: Layout view, it will not change

## Slide 58
Scale

## Slide 59
Use caution when employing bar scales on smaller scale maps
    Scale is only accurate along standard lines
Scale is accurate only along the standard line
Scale
Notes: Miller Cylindrical

## Slide 60
The maximum distance value should always be round and easy to work with
Incorporate a unit of measure that is appropriate for the intended audience
  Incorporate both miles and kilometers if necessary
  Choose a unit of measure that is appropriate for the maximum value
Scale

## Slide 61
Don’t use an “extension scale” unless the map user requires it
  Shows finer subdivisions of the scale bar allows for smaller distance measurements
  The extension scale can be useful when employing a specific method of map measurement, but it can also be a source of confusion
And the “checkerboard” serves no purpose, other than to attract attention.
Scale
Notes: An extension scale which shows finer subdivisions of the scale bar allows for smaller distance measurements.
If you have decided to use a scale bar and you have more than one mapped area (e.g., the coterminous U.S., Alaska and Hawaii), each mapped area requires its own scale bar if they are shown at different scales.

## Slide 62
The style of the bar scale should be simple and subtle; it should not attract attention
  Bulky and complex designs should be avoided
  Line weights should be thin and type should be among the smallest on a map
  Avoid the use of bold and italic type styles
Scale

## Slide 63
Poorly Designed
Well Designed
Discussion
Which group is better? And Why?

## Slide 64
Scale
The compact form is more modern, the linear form is classic.
Peterson, 2021

## Slide 65
The indication of north on a map
Orientation can be indicated by a
  North Arrow
  Graticule (a system of grid lines, normally representing longitude and latitude)
Orientation

## Slide 66
A north arrow is not required on every map!
  The orientation of maps with north at the top is a long-standing tradition
  It is assumed that “north is at the top” of most modern maps
Orientation

## Slide 67
Include an indication of orientation if
  The map is not oriented with geographic or “true” north at the top
Orientation

## Slide 68
Include an indication of orientation if
  The map is intended for use in navigation, surveying, orienteering, etc.
Orientation

## Slide 69
Include an indication of orientation if
  Geographic features are oriented in a manner that might confuse the map user
Orientation

## Slide 70
A graticule indicates direction through the orientation of grid lines
  Typically meridians that run north–south
  The graticule can also provide positional information, such as latitude and longitude
Orientation

## Slide 71
Use caution when using north arrows on smaller scale map
  The direction of north can differ greatly in the maps with azimuthal and conic projection
N
N
N
Orientation

## Slide 72
Use caution when using north arrows on smaller scale maps
  Place the graticules beneath land masses
Orientation
Peterson, 2021

## Slide 73
The style of the north arrow and graticule should be simple and subtle; they should not attract attention
  Bulky and complex designs should be avoided
  Line weights should be thin and type should be among the smallest on a map
  Only north should be indicated
Orientation

## Slide 74
Poorly Designed
Well Designed
Discussion
Which group is better? And Why?

## Slide 75: RELATIVE TYPE SIZES FOR CERTAIN MAP ELEMENTS
Sizes should decrease as follows
  Title
  Subtitle
  Legend Heading
  Legend Definitions
  Source, scale, north arrow
Use the same type family for ALL map elements!

## Slide 76
Which one is better?
Notes: A noisy, inefficient communicator
A simple, efficient communicator

## Slide 77
Thank you!