## Slide 1: Lecture 07 Map Elements lecture
Instructor: Yanan Wu
fALL 2025

## Slide 2: 7.1 MAP ELEMENTS

## Slide 3
Allows the map user to determine where data were obtained
  Sources of base information are normally omitted from thematic maps
Should be formatted similar to a standard bibliographic reference, but is often more concise and less formal
Data source

## Slide 4
The words “Data Source:” or “Source:” should be included to avoid ambiguity
  The data source indicates where data came from, not map authorship
A separate block of type can be used to indicate map authorship
The style of the data source should be plain and subtle
Publication names should be italicized
Multiple lines of type should be horizontally centered (center aligned)
Data source

## Slide 5
Data source

## Slide 6
The data source should be among the smallest type on a map
  Its purpose is to inform the curious, not to attract attention
Center it below the legend
  Or tuck it into a lower corner
Data source

## Slide 7
Indicates the amount of reduction that has taken place on a map, or allows the map user to measure distances
Can take three forms
  Representative Fraction (1:24,000)
  Verbal Scale (“One Inch to the Mile”)
  Bar Scale or Scale Bar
Scale
Notes: larger scale: greater detail and smaller area
Smaller scale: less detail and larger area

## Slide 8
Scale

## Slide 9
The bar scale is preferred format for inclusion on a thematic map
  Resembles a ruler
  Remains true when a map is enlarged or reduced (representative fractions and verbal scales don’t)
  Include if distance information can enhance the map user’s understanding of the theme
Scale
Notes: Layout view, it will not change

## Slide 10
Scale

## Slide 11
Use caution when employing bar scales on smaller scale maps
    Scale is only accurate along standard lines
Scale is accurate only along the standard line
Scale
Notes: Miller Cylindrical

## Slide 12
The maximum distance value should always be round and easy to work with
Incorporate a unit of measure that is appropriate for the intended audience
  Incorporate both miles and kilometers if necessary
  Choose a unit of measure that is appropriate for the maximum value
Scale

## Slide 13
The style of the bar scale should be simple and subtle; it should not attract attention
  Bulky and complex designs should be avoided
  Line weights should be thin and type should be among the smallest on a map
  Avoid the use of bold and italic type styles
Scale

## Slide 14
Poorly Designed
Well Designed
Discussion
Which group is better? And Why?

## Slide 15
Scale
The compact form is more modern, the linear form is classic.
Peterson, 2021

## Slide 16
Explore Scale in ArcGIS Pro
Scale

## Slide 17
The indication of north on a map
Orientation can be indicated by a
  North Arrow
  Graticule (a system of grid lines, normally representing longitude and latitude)
Orientation

## Slide 18
A north arrow is not required on every map!
  The orientation of maps with north at the top is a long-standing tradition
  It is assumed that “north is at the top” of most modern maps
Orientation

## Slide 19
Include an indication of orientation if
  The map is not oriented with geographic or “true” north at the top
Orientation

## Slide 20
Include an indication of orientation if
  Geographic features are oriented in a manner that might confuse the map user
Orientation

## Slide 21
A graticule indicates direction through the orientation of grid lines
  Typically meridians that run north–south
  The graticule can also provide positional information, such as latitude and longitude
Orientation

## Slide 22
Use caution when using north arrows on smaller scale map
  The direction of north can differ greatly in the maps with azimuthal and conic projection
N
N
N
Orientation

## Slide 23
Use caution when using north arrows on smaller scale maps
  Place the graticules beneath land masses
Orientation
Peterson, 2021

## Slide 24
The style of the north arrow and graticule should be simple and subtle; they should not attract attention
  Bulky and complex designs should be avoided
  Line weights should be thin and type should be among the smallest on a map
  Only north should be indicated
Orientation

## Slide 25
Poorly Designed
Well Designed
Discussion
Which group is better? And Why?

## Slide 26: RELATIVE TYPE SIZES FOR CERTAIN MAP ELEMENTS
Sizes should decrease as follows
  Title
  Subtitle
  Legend Heading
  Legend Definitions
  Source, scale, north arrow
Use the same type family for ALL map elements!

## Slide 27: 7.2 Lab session

## Slide 28: Lab 05: standardization and classification
Due by Midnight (11:59 pm) on Monday, OCT 06, 2025
Submit a word document only include question and answer