## Slide 1: Lecture 12 geocoding lecture
Instructor: Yanan Wu
fALL 2025

## Slide 2: 12.1 geocoding

## Slide 3
What is geocoding?
Why geocoding?
Geocoding requirement
Geocoding process
    Geocoding errors and solutions
    Other geocoding layers
Overview

## Slide 4
What is geocoding?
Geocoding is the process of converting location descriptions, such as addresses, into geographic coordinates that can be displayed on a map.
Address Matching assigns spatial coordinates (explicit location) to the Addresses (implicit location).

## Slide 5
What is geocoding?
Displays tabular data containing addresses as points on a map.
https://guides.library.illinois.edu/Geocoding

## Slide 6
Geocoding requirement
Geocoding requires two sets of data
  A tabular address: individual street address is in a table.
  A reference database: consists of a street map and attributes for each street segment such as the street name, address ranges, and ZIP codes.

## Slide 7
Geocoding requirement
Geocoding requires two sets of data
  A tabular address: source data
    Formatted
    Abbreviations should be standardized and grammatical errors corrected
    When geocoding street addresses, data must include an address field with street number and name, and can include one or more of the following:
      Street prefix direction (W. Redlands Blvd.)
      prefix type (Avenue B)
      street type (W. Redlands Blvd.)
      suffix direction (Park Ave. West.)

## Slide 8
Geocoding requirement
Geocoding requires two sets of data
  A tabular address: source data
    Street intersections may also be included in the address field. (Main St. & Ave A)

## Slide 9
Geocoding requirement
Geocoding requires two sets of data
  A tabular address: source data
    ArcGIS require your address information to be contained in a single field
https://www.slideserve.com/nysa/geocoding-1313468-powerpoint-ppt-presentation

## Slide 10
Geocoding requirement
Geocoding requires two sets of data
  A reference database: destination data
    In most cases, the reference database in the U.S. is some variant of the Topologically Integrated Geographic Encoding and Referencing (TIGER) files produced by the U.S. Census Bureau.
    TIGER/Line files provide information on streets, rivers, railroads, and other line features, where they intersect, and the areas they enclose, in a form that can be processed by a computer.

## Slide 11
Geocoding requirement
Geocoding requires two sets of data
  A reference database
    TIGER/Line files to maintain the Topology
Notes: lane

## Slide 12
Geocoding requirement
Geocoding requires two sets of data
  A reference database
    TIGER/Line files

## Slide 13
Geocoding requirement
Geocoding requires two sets of data
  A reference database
    TIGER/Line files
https://www.e-education.psu.edu/natureofgeoinfo/book/export/html/1730

## Slide 14
Geocoding process
Address matching process consists of three phases: preprocessing, matching, and plotting.
  The preprocessing phase involves parsing and addressing standardization
  In the matching phase, the geocoding engine matches the address against a reference database
  If an address is judged to be matched, it is plotted as a point feature by interpolating where the address falls within the address range

## Slide 15
Geocoding process

## Slide 16
Geocoding process

## Slide 17
Geocoding process
A geocoding engine has provisions for relaxing the matching conditions but uses a scoring system to quantify the matches at the same time.
Because of the various matching options, we can expect to run the geocoding process more than once.

## Slide 18
Geocoding process
(125-101)/(199-101) = 0.24
So, it is placed 24% along the given length for the segment
125

## Slide 19
Individual activity 12-1
If the HN is 160, where it should be placed?

## Slide 20
Geocoding process
Address matching requires an Address Locator which establishes explicit methods for matching (geocoding) address data to a specified reference database.
The result of geocoding is expressed as the percentage of addresses matched
For crime mapping and analysis, 85% matching score is required.

## Slide 21
Geocoding errors and solutions
  Data Entry Errors
  Fidth Avenue
  Sawmill Run
  Place Names
  White House, Heinz Field, Empire State Building
  Intersections
  5th AV and Craig ST
  Post Office Boxes
  P.X.Box 125

## Slide 22
Geocoding errors and solutions
  Use postal address standards
  Publication 28 of the U.S. Post office provides standard street address formats
  Use standard intersection connectors
  & | @
  Put street intersections in the address field
  Forbes AV & Craig ST
  Grant ST & 5th AV
  E North Star RD & Duncan AV
  Connectors
  Any unusual character (e.g., &, @, |) be consistent

## Slide 23
Polygon Geocoding
Points created at zip code centroids

## Slide 24
Geocoding errors and solutions
Use Alias Table

## Slide 25
Polygon Geocoding
Polygon features can be identified by their parcel numbers, postal zip, or zip +4 codes

## Slide 26: In-class activity
Geocode Address

## Slide 27: 12.2 Lab session

## Slide 28: Lab 08: Vector Analysis
Due by Midnight (11:59 pm) on Monday, Nov 10, 2025
Submit a word document only include question and answer