## Slide 1: WEEK 03 Projection
Instructor: Yanan Wu
fALL 2025

## Slide 2: 2.1 KEY ASSUMPTION

## Slide 3
Datum
Transformation
  Converting coordinates from one datum to another
    Shift origin
    Scale
    rotation
Bolstad, 2019

## Slide 4: MAP PROJECTION
Conversion from geographic to projected coordinates
Bolstad, 2019

## Slide 5
Developable Surfaces
  Geometric surface that can be flattened
Cylindrical Projections = Cylinder Conic Projections = Cone Azimuthal Projections = Plane
Map projection
Notes: In order to flatten the Earth, coordinates on the globe must be mathematically transformed or moved to a geometric surface that can be flattened. These are called developable surfaces.
The most commonly used surfaces are cylinders, cones, and planes. Cylindrical projections use cylinders, conic projections use cones, and azimuthal projections use planes.
There are other shapes available or shapes can be combined. Here, we will focus on just these most commonly used surfaces.
Note that all three of these surface can be flattened. If you cut a cylinder, it can be folded out to a plane. A cone can be folded out into a fan shape.

## Slide 6
Developable Surfaces
  Geometric surface that can be flattened
Map projection
Bolstad, 2019

## Slide 7
Cylindrical Projection
This creates a rectangular grid
Distortion increases toward the poles — shapes and areas get stretched
Good for navigation
* Creation of cylindrical projection

## Slide 8
Plane projection
Plane positioned at pole
Grid:
  Longitude: straight, radiating
  Latitude: circles
Distortion increases away from center ("principal point")
Good for polar regions
Can't show more than half the world.
Plane projection

## Slide 9
Conic projection
Hold cone over pole
Grid:
  Longitude: straight, converge
  Latitude: curve
  Distortion increases away from standard parallel
Good for Mid-latitudes
Conic projection

## Slide 10
All map projections produce distortions of at least one of the following:
  Shape
  Area
  Distance
  Direction
Shape
Area
Distance
Direction
3D Earth
2D Map
Map projection
Notes: Since the curved, 3D surface of the Earth is converted to a flat space, some distortions will be produced.
It is not possible to convert a curved 3D surface into a flat surface without some distortions.
Specifically, map projections can produce distortions in feature shape, relative area of features, distance between features, and direction between locations.
The type and magnitude of the distortions produced depends on the projection used.

## Slide 11
All map projections produce distortions of at least one of the following:
  Shape
  Area
  Distance
  Direction
Map projection
Bolstad, 2019
Mercator
Transverse Mercator

## Slide 12
Map projection
Why all world maps are wrong?

## Slide 13
Type
Conformal Projections: preserves local angles and shape
Equivalent Projections: represents areas in correct relative size
Equidistant Projections: maintains consistent scale or distance along certain lines
Azimuthal Projections: maintains certain accurate directions relative to certain vantage point
Conformal and equivalent projections’ properties are mutually exclusive
Conformal and equivalent projections’ properties are global properties
Equidistant and azimuthal projections’ properties are local properties and may be true only from or to the center of the map projection
Map projection
Notes: Four broad types of projections exist based on what map properties are maintained.
Conformal projections maintain local angles and shapes. Equivalent projections maintain areas of features in correct relative size. Both are global properties, or shape or size can be maintained across the entire globe not just for specific areas. Also, these properties are mutually exclusive. Or, you cannot maintain both shape and relative size.
Equidistant projections maintain scale or distance along certain lines while azimuthal projections maintain accurate directions relative to a certain vantage point. Equidistant and azimuthal properties are local properties and may be true only from or to the center of the map projection. You cannot maintain distance or direction between all points in the map space.

## Slide 14
  Cylindrical conformal projection
  Parallels and meridians cross at right-angles
World projection - Mercator
Tissot Indicatrix
Distort size but not shape
  Without any distortions, the circles will all be the same shape and size
Q: In the projection, are the circles distorted in shape or in size?
🤔
Notes: Mercator projections are examples of cylindrical projections that are conformal, or maintain shape and local angles. (To preserve individual angles describing the spatial relationships, a Conformal projection must show the perpendicular graticule lines intersecting at 90-degree angles on the map)
Relative size tends to be heavily distorted. For example, the Tissot Indicatrix suggests that sizes close to the poles are much larger than they should be in comparison to equatorial features. Remember from the example above that Greenland is actually smaller than Australia.
In Mercator projections, parallels and meridians will cross at right-angles.

## Slide 15
  Modification of Mercator projection that is commonly used for web maps
  Bing Maps, OpenStreetMap, Google Maps, MapQuest, ArcGIS Online
Map projection – Web Mercator
http://cartonerd.blogspot.com/2014/08/web-mercator-and-comparisons.html
Notes: Web Mercator is a modification of the Mercator projection that is commonly used in web maps including Bing Maps, OpenStreetMap, Google Maps, MapQuest, and ArcGIS Online.
It uses a true sphere as opposed to a spheroid.
One reason this projection is used on the web is that it is easy to generate tiles from data since latitude and longitude lines intersect at right angles.

## Slide 16
  Equivalent projection
  Pseudo cylindrical
  Not based on developable surface
Map projection - Mollweide
Distort shape but not size
Q: In the projection, are the circles distorted in shape or in size?
🤔
Notes: Mollweide is an example of a equivalent projection that maintains relative size or area but distorts shape and local angles.
It is pseudosylindrical, which means that is uses multiple cylinders as opposed to one in an attempt to further minimize distortions.

## Slide 17
Class Activity
Explore the true size tool https://thetruesize.com/#.
  Does Greenland look larger or smaller than Brazil on the basemap?
  Search for ‘Greenland’
  Drag Greenland over Brazil to compare their areas

## Slide 18
Not Projected
Mercator
US projections
Map projection
Notes: We will now discuss continental-scale projections using the United States as an example.
The first image shows the US as not projected. Or, latitude and longitude are being treated like Cartesian coordinates in flat space. This results in some extreme distortions and should be avoided.
The second image shows a Mercator projection for the US. Here, shape and local angle is maintained but relative size is distorted.

## Slide 19
Albers Equal Area
Lambert Conformal Conic
US projections
Map projection
Notes: When creating maps of the US, I prefer to use Albers Equal Area or Lambert Conformal Conic.

## Slide 20
US projections: Albers Equal Area
  Conic
  Equivalent
  Maintains area
  Distort shape and local angles
Map projection
Notes: Albers Equal Area uses a conic developable surface with two standard parallels. It is equivalent, so it maintains relative size but distorts shape and local angles.
However, distortions are generally pretty minimal.

## Slide 21
US projections: Lambert Conformal Conic
  Conic
  Conformal
  Maintains shape and local angles
  Distorts local size
Map projection
Notes: Lambert Conformal Conic also uses a cone with two standard parallels. Since it is conformal it maintains shape and local angles but distorts local size.
However, distortions are minimal.
So, if I want to created a map of the US that maintains relative size, I tend to use Albers Equal Area. If I want to maintain shape, I will use Lambert Conformal Conic.

## Slide 22: Example Scenarios
An airline wants to create flight maps across the contiguous U.S.
The U.S. Census Bureau makes a map of population density by state.
Q: Which projection we should use in above scenario?
🤔

## Slide 23
Examples
  Projected coordinate systems do not use longitude and latitude to measure locations
  Instead, they use map units of the projection itself:
  Meters (UTM, Albers, most others)
  Feet (State Plane, few others)
Map projection

## Slide 24
Universal Transverse Mercator (UTM)
  60 zones
  Location provided in meters as Easting and Northing
  Northing: meters north of equator
    In northern hemisphere, equator is assigned a value of 0 meters, add as you go up
    In southern hemisphere, equator is assigned a value of 10,000,000 meters, subtract as you go down
  Easting: distance from central meridian in UTM zone
    Central meridian is assigned a value of 500,000 meters
    Add as you go east
    Subtract as you go west
Map projection
Notes: We will now discuss projections that are appropriate at more local scales, such as for states, counties, or cities.
Universal Transverse Mercator is a set of projections that are commonly used at these scales.
This is not one system but a set of systems in which the Earth is broken into 60 zones.
Within each zone coordinates are provided in length units, generally meters, as northing and easting.
Northing measures up and down or north to south. In the northern hemisphere, the equator is assigned a value of 0 meters, and you add as you move north. So, this is effectively the distance from the equator. In the southern hemisphere, the equator is assigned a value of 10,000,000 meters, and you subtract as you move south.
Easting is calculated relative to the central meridian or center line in each zone. The central meridian is assigned a value of 500,000 meters, and you add as you move east of it and subtract if you move west.

## Slide 25
Universal Transverse Mercator (UTM)
Map projection
Bolstad, 2019
Notes: The UTM systems break the Earth into 60 zones vertically.
Each zone is only appropriate for areas within it. You should not project the entire Earth to a single UTM projection.
Easting values will be defined relative to the central meridian in each zone.
In the US, the zone number increases as you move east and decreases as you move west.
The majority of Arkansas is in UTM Zone 15 North. So, this is a common projection for Arkansas. So, Arkansas generally uses a geographic coordinate system of NAD83 or WGS84 and a projected coordinate system of UTM Zone 15 North.
Some states fit well into a single UTM zone, for example Nevada, Utah, and Alabama. Others do not, such as California or Pennsylvania.
For states that do not fit well into one UTM zone, other projections are generally used to display them.

## Slide 26
State Plane Coordinate System
  125 geographic zones designed for specific regions in the United States
  Zones follow county boundaries
  city- to county-scale
https://www.e-education.psu.edu/natureofgeoinfo/c2_p26.html
Map projection
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 27
State Plane Coordinate System
  Transverse Mercator projection (for states with long north-south axis)
  Lambert conformal conic projection (for states with long east-west axis)
Map projection
Lambert conformal conic
Transverse Mercator
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 28
State Plane Coordinate System
  The zones may change!
Map projection
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 29
It is not a coordinate system, but used widely for land parcels since 1800s
  Divided lands by north-south lines, 6 miles apart
  East-west lines were surveyed perpendicular to those north-south lines, also at 6 miles intervals
  30 states adopted PLSS
Public Land Survey System
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 30
Place roads, powerlines, and other public services
Public Land Survey System
Bolstad, 2019
Notes: The PLSS is important because:
1) The PLSS lines are often property boundaries, they form natural corridors in which to place roads, powerlines, and other public services; they are often evident on the landscape. Many road intersections occur at PLSS corner points, and these can be viewed and referenced on many maps or imagery used for GIS database development efforts. Further, PLSS corners are sometimes resurveyed using high precision methods to provide property line control, particularly when a GIS is to be developed.

## Slide 31
Projection used is related to type of map and area covered by map (extent)
Continental-scale data (North America)
  Geographic projection (decimal degrees)
  Lambert Conformal Conic
  Albers Equal Area
State-scale data (Arkansas)
  UTM Projection, Zone 15N
  County, city-scale data
  State Plane
Map projection
Notes: The best map projection to use partially depends on the extent being mapped or the scale of the map.
We will now investigate some common map projections that can be used at different scales.
Note that all maps and spatial data layers will be referenced to a datum or geographic coordinate system.
If the map or data have been projected, they will also have a projected coordinate system where measurements are made in length units as opposed to angles.
We will begin with a discussion of some common global-scale projections followed by continent- and sate-scale options.

## Slide 32
Should use same projection and datum for all data
Use projection appropriate for scale and extent
Think about what map properties are maintained or distorted
Best Practice
Notes: This slide highlights best practices for working with projections.
First, it is generally best to use the same projection for all data layers in a map or project to avoid any issues with misalignment.
You should use a projection appropriate for the scale and extent of the map. For example, you would not use a specific UTM zone to project the entire globe. On the other hand, a global projection would not be the best choice for data just within Arkansas.
You should also think about what map properties are maintained or distorted. If you are interested in maintaining relative size, then you should use an equivalent projection.

## Slide 33
ArcGIS can apply a projection transformation on-the-fly
So, it is not always necessary to reproject data
Okay if you are visualizing the data
Need to reproject if you plan to perform an analysis
Projection-on-the-Fly (ArcGIS)
Notes: Note that ArcGIS Pro can apply a projection transformation on-the-fly or in memory.
So, data that are read into a map that are in a different projection than the map can be reprojected to match the map on-the-fly.
So, it is not always necessary to reproject data if you are simply visualizing it or making a map layout.
However, I suggest transforming all data layers into the same projection if you plan to perform spatial analysis.

## Slide 34
Thank you!