## Slide 1: WEEK 03 Datum
Instructor: Yanan Wu
fALL 2025

## Slide 2: 3.1 Datum

## Slide 3
Datum
  Shape of Earth
  Geoid
Coordinate system
  Geographic coordinate systems
  Projected coordinate systems
Overview

## Slide 4: Why are datums important?
Tracking land-based wildlife with GPS

## Slide 5
Geodesy
  Science of measuring Earth’s shape
https://commons.wikimedia.org/wiki/File:Geoundnsrp.png
Shape of the Earth
Notes: All spatial data must be referenced to the surface of the Earth so that they draw at the correct location in the map space.
This means that we need models of the Earth to which we can reference maps and data.
This is a component of the science of geodesy, which relates to measuring the Earth’s shape and positions on it.

## Slide 6
Oblate spheroid
  Equator has larger circumference than meridians
  Mass not evenly distributed
Shape of the Earth
Notes: To begin, the Earth is not a perfect sphere. Instead, it is an oblate spheroid.
It is wider than it is tall. Or, the circumference of the equator is longer than the circumference of the prime meridian or any meridian.
This results from the centrifugal forces arising from the planet’s rotation.
Further, mass is not evenly distributed throughout the Earth.
So, the Earth is actually a fairly irregular shape, which results in complexity in regards to producing reference systems by which to reference our maps and data against it.

## Slide 7
Oblate spheroid
  Equator has larger circumference than meridians
  Mass not evenly distributed
Shape of the Earth
Notes: To begin, the Earth is not a perfect sphere. Instead, it is an oblate spheroid.
It is wider than it is tall. Or, the circumference of the equator is longer than the circumference of the prime meridian or any meridian.
This results from the centrifugal forces arising from the planet’s rotation.
Further, mass is not evenly distributed throughout the Earth.
So, the Earth is actually a fairly irregular shape, which results in complexity in regards to producing reference systems by which to reference our maps and data against it.

## Slide 8: Modeling the Earth
True Earth surface
Geoid (Includes ocean)
Ellipsoid
Earth Model
Notes: In order to model the Earth, simplification is required.
The true Earth surface need to be generalized. First, it is generalized to a geoid.
This is further simplified to an ellipsoid.
We will explore these concepts now.

## Slide 9
https://en.wikipedia.org/wiki/Geoid
Geoid: gravity-related vertical reference
In geodesy, the geoid is an imaginary sea (mean sea level) that covers the entire Earth
It is not affected by wind, waves, the Moon, or forces other than Earth’s gravity. .
Notes: The geoid models the distribution of mass across the Earth, which is not uniform. The Earth is a bumpy surface.
This is partially accomplished by measuring gravitational forces across the globe.
A conceptualization of the geoid is a globe that is fully covered by water or has no continental masses.
Because there are differences in mass and gravitational forces across the globe, the water surface would not be smooth.
Instead, it would be a smoothly undulating shape.
This smoothly undulating shape that takes into account the distribution of mass is called the geoid.
The geoid surface can them be used as a reference for zero elevation.

## Slide 10
Geoid Height
Which areas have higher values of Geoid height?
🤔

## Slide 11: Geoid height

## Slide 12: What Do We Really Mean by 'Sea Level'? A Journey into the Geoid

## Slide 13
We need a mathematically simple model of the Earth’s Surface
We use an ellipsoid / spheroid
There are different ellipsoids/ spheroids used
Combined with ground survey data, we call these datums
Datum
Notes: The geoid is still a complex shape that cannot be modeled with a simple mathematical equation.
So, it is further simplified to an ellipsoid or spheroid model of the Earth.
This is a mathematical model that approximates the geoid as a smooth surface. Basically, this is a 3D ellipse.
Combining this model with ground survey data allows us to produce datums.
These datums serve as the reference systems by which we represent locations on Earth’s surface.
Our map and geospatial data will be referenced to one of these models.
The arc lengths may be measured by surface surveys, and the angles from astronomical observations

## Slide 14: What is datum?

## Slide 15: Horizontal datum
A mathematical model and reference system
It defines how to pinpoint locations on the Earth's surface using latitude and longitude coordinates

## Slide 16: The World at Zero: Equator & Prime Meridian
                Using Google Earth, find the location at the intersection of the Equator (0° latitude) and the Prime Meridian (0° longitude). Does this point fall on land or in the ocean?
Identify one country that lies near the Prime Meridian (0° longitude).
Identify one country that lies near the Equator (0° latitude).
* Click view – show gridlines to display gridlines on earth

## Slide 17
Common Horizontal Datum
NAD27: North American Datum of 1927
NAD83: North American Datum of 1983
  NAD83(xx), xx represents year, version of datum adjustment
  NAD83(HARN/HPGN): High Accuracy Reference Networks or High Precision Geodetic Networks
WGS84: World Geodetic System 0f 1984
  WGS84(xx)
ITRF: International Terrestrial Reference Frames
  ITRF89, ITRF90, ITRF91
Notes: There are different datums by which we reference are horizontal measurements or coordinates on the Earth.
Examples include the North American Datum of 1927 (or NAD27), the North American Datum of 1983 (or NAD83), and the World Geodetic System of 1984 (or WGS83).
In North America, it is common to reference data against NAD83 or WGS84.
Global Navigation Satellite Systems, or GNSS, often make use of WGS84 as a worldwide datum.
Again, think of these as different models of the Earth, all of which are simplifications.
The HARN and subsequent NAD83 adjustments are largely satellite-based, including WGS84 and ITRF

## Slide 18
Datum
WGS84 and ITRF can be considered equivalent for most purpose, as difference between them since 1995 are generally only a few centimetres
Bolstad, 2019
Notes: Tectonic movement, crustal deformation

## Slide 19: Which datum google map use?
NAD27 or WGS84?

## Slide 20: Vertical datum
A standardized reference surface used to define elevations and depths on the Earth's surface, serving as a "zero" point for measurements.

## Slide 21: Vertical datum - examples
Elevation of cities and landmarks 🏔️
– Example: The elevation of Denver (“Mile High City”) is measured relative to NAVD88 in the U.S.
Flood levels & floodplain mapping 🌊
– FEMA flood maps use vertical datums (e.g., NAVD88) to define the Base Flood Elevation (BFE).

## Slide 22
Relationship between terrain, an datum, and an ellipsoid
Notes: NGS (National Geodetic Survey),Triangulation survey
For the most of the past 150 years, the most accurate observations were referenced to the Sun, stars, or other celestial bodies
Every few years

## Slide 23
NGVD29: National Geodetic Vertical Datum of 1929
  No geoid, mean sea level
NAVD88: North American Vertical Datum of 1988 (NAVD88)
  GEOID03, GEOID09, GEOID12B
Common vertical datum
Notes: Example vertical datums in North America include the National Geodetic Vertical Datum of 1929 (NGVD29) and the more recent North American Vertical Datum of 1988 (NAVD88).
As technologies advance, updated versions of horizontal and vertical datums will be released.
GEOID18 is intended for use with coordinates in the North American Datum of 1983 (2011) [NAD 83 (2011) epoch 2010.00]. It provides orthometric heights consistent with the North American Vertical Datum of 1988 (NAVD 88), the Puerto Rico Vertical Datum of 2002 (PRVD02), or the Virgin Islands Vertical Datum of 2009 (VIVD09).

## Slide 24
Datum Inconsistent

## Slide 25
Datum Pairing
Pairing for horizontal and vertical datums for North America
Notes: Example vertical datums in North America include the National Geodetic Vertical Datum of 1929 (NGVD29) and the more recent North American Vertical Datum of 1988 (NAVD88).
As technologies advance, updated versions of horizontal and vertical datums will be released.
GEOID18 is intended for use with coordinates in the North American Datum of 1983 (2011) [NAD 83 (2011) epoch 2010.00]. It provides orthometric heights consistent with the North American Vertical Datum of 1988 (NAVD 88), the Puerto Rico Vertical Datum of 2002 (PRVD02), or the Virgin Islands Vertical Datum of 2009 (VIVD09).

## Slide 26: 2.2 coordinate system

## Slide 27
Coordinates on a Sphere
  Latitude and Longitude
  Specified as angles or degrees
  Latitude: Angles from equator
    Range 0-90 N/S
  Longitude: Angles from prime meridian
    Range 0-180 E/W
Geographic Coordinate Systems
© 2013 by John Wiley & Sons, Inc. All rights reserved.
Notes: Coordinates on Earth are measured in degree units relative to the center of the Earth.
Latitude is measures as an angle of rise relative to the center of the Earth while longitude represents angles of rotation around the center of the Earth.
Note that it is not easy to make measures of distance using lengths on a spherical surface.

## Slide 28
Geographic Coordinate Systems
Latitude (Parallels):
  Measures north to south
  90° in each hemisphere
  Increases as you go north in the northern hemisphere
  Increases as you go south in the southern hemisphere
  Zero in Equator
https://commons.wikimedia.org/wiki/File:Latitude_and_Longitude_of_the_Earth.svg
Notes: Latitude measures north to south or up and down. There are 90° of latitude in each hemisphere. The value increases as you move north or south relative to the equator. The equator has a latitude of 0° and the poles have a latitude of 90°.

## Slide 29
Geographic Coordinate Systems
Longitude (Meridians)
  Measures east to west
  180° in each hemisphere
  Increases as you go east in the eastern hemisphere
  Increases as you go west in the western hemisphere
  Zero is Prime Meridian, going through Greenwich, England
https://commons.wikimedia.org/wiki/File:Latitude_and_Longitude_of_the_Earth.svg
Notes: Longitude measures east to west or side to side. There are 180° of longitude in each hemisphere, east and west. Longitude increases has you move west in the western hemisphere and increase as you move east in the eastern hemisphere. 0° longitude is refined relative to the prime meridian which passes through Greenwich, England.
It makes sense to use the equator to represent 0° latitude. The 0° reference for longitude is somewhat arbitrary.
We can specify the northern or southern hemispheres for latitude by including an “N” or “S” with the measurements. For longitude, we can use “E” or “W”.
In software, this can be problematic due to the mix of numbers and letters. So, instead we tend to use positive angles to represent the northern or eastern hemispheres and negative angles to represent the southern or western hemispheres.
Coordinates referenced to a datum representing the 3D Earth or globe are known as geographic coordinate systems as opposed to projected coordinate systems, which will be discussed later.

## Slide 30
1 Degree = 60 Minutes = 3600 Seconds
  ˚ = Degrees
  ‘ = Minutes
  “ = Seconds
  1.5 ˚ =1 ˚ 0.5X60’= 1 ˚ 30’
  1 ˚ 30’ = 1° + (30’/60’) = 1.5°
Geographic Coordinate Systems
Notes: One degree of latitude or longitude can be a large distance. So, in order to provide precise measurements, we need to be able to further divide degrees into smaller units.
A degree can be divided into minutes and second, similar to an hour on a clock.
1 degree equals 60 minutes or 3600 seconds.
We can also use decimal degrees as opposed to minutes and seconds.
It is possible to convert between degrees, minutes, and second and degrees and decimal degrees.

## Slide 31
Advantages:
  Accurate representation
  Latitude and longitude lines
  Without distortion
  Disadvantages
    Expensive to make
    Cumbersome to handle and store
    Difficult to measure distance
    Not fully visible at one view
Geographic Coordinate Systems
Image from Google Earth
Notes: There are some advantages to modeling the Earth as a 3D globe. First, this is an accurate representation in which map features and latitude and longitude lines can be plotted without distortion.
However, there are some disadvantages. Making globes can be expensive. They are also cumbersome to handle and store. It is also not easy to make distance measurements on the curved surface of the globe. Duo to the 3D nature of a globe, it is not possible to view the entirety of Earth’s surface from a single vantage point.
So, we need a means by which to represent the curved, 3D Earth in a flat map space. We do this using projections, which we will discuss next.

## Slide 32
Map projections allow us to view the 3D Earth on a 2D surface
  Earth is mathematically projected to a surface that can be made flat
  We now make measurements in distance or length units as opposed to degrees
Projected Coordinate Systems
https://commons.wikimedia.org/wiki/File:Cartesian_coordinate_system_(comma).svg
Notes: Instead of using a the 3D spherical globe, we can mathematically transform the Earth into a flat map space.
Now, instead of making measurements of distance or length in angles, we can make measurements in length units.
These 2D surfaces are known as projected coordinate systems or map projections.
They allow us to make measurements in a Cartesian coordinate system on a plane.

## Slide 33
  They allow us to make measurements in a Cartesian coordinate system on a plane
  These 2D surface are known as map projections.
Projected Coordinate Systems
https://commons.wikimedia.org/wiki/File:Cartesian_coordinate_system_(comma).svg

## Slide 34: Geographic vs Projected Coordinate Systems
Image from ArcGIS API for JavaScript
Image from ArcGIS API for JavaScript
Notes: This slide provides an example of the difference between geographic and projected coordinate systems.
The globe provides a 3D representation of the Earth where measurements are made in angles.
In contrast, projections are 2D and allow for measurements to be made in Cartesian coordinate space.

## Slide 35: Well-Known ID - wkid
Defines a Coordinate System
  It identifies a specific system for measuring locations on the Earth's surface, including geographic coordinates (like latitude and longitude) and projected coordinates.
  Examples of WKIDs:
  4326 (WGS 84)

## Slide 36
Datum/Projection Info in ArcGIS
Notes: Datum and sometimes projection information are associated with maps and geospatial data layers.
In ArcGIS Pro, datum and projection information for a layer can be found in the Source tab.
We will talk about projections later in this module.

## Slide 37: 2.3 Lab session

## Slide 38: Lab 02: Introduction to ArcGIS Pro
Due by Midnight (11:59 pm) on Monday, Sep 8, 2025
Submit a word document only include question and answer