## Slide 1: WEEK 03 Datum and Projection
Instructor: Yanan Wu
fALL 2025

## Slide 2: 2.1 KEY ASSUMPTION

## Slide 3
Datum
  Shape of Earth
  Geoid
Coordinate system
  Geographic coordinate systems
  Projected coordinate systems
Projections
  Plane projection
  Conic projection
  Cylindrical projection
  Examples: Global, continental, and state scales
Overview

## Slide 4
Geodesy
  Science of measuring Earth’s shape
https://commons.wikimedia.org/wiki/File:Geoundnsrp.png
Shape of the Earth
Notes: All spatial data must be referenced to the surface of the Earth so that they draw at the correct location in the map space.
This means that we need models of the Earth to which we can reference maps and data.
This is a component of the science of geodesy, which relates to measuring the Earth’s shape and positions on it.

## Slide 5
Oblate spheroid
  Equator has larger circumference than meridians
  Mass not evenly distributed
Shape of the Earth
Notes: To begin, the Earth is not a perfect sphere. Instead, it is an oblate spheroid.
It is wider than it is tall. Or, the circumference of the equator is longer than the circumference of the prime meridian or any meridian.
This results from the centrifugal forces arising from the planet’s rotation.
Further, mass is not evenly distributed throughout the Earth.
So, the Earth is actually a fairly irregular shape, which results in complexity in regards to producing reference systems by which to reference our maps and data against it.

## Slide 6
Oblate spheroid
  Equator has larger circumference than meridians
  Mass not evenly distributed
Shape of the Earth
Notes: To begin, the Earth is not a perfect sphere. Instead, it is an oblate spheroid.
It is wider than it is tall. Or, the circumference of the equator is longer than the circumference of the prime meridian or any meridian.
This results from the centrifugal forces arising from the planet’s rotation.
Further, mass is not evenly distributed throughout the Earth.
So, the Earth is actually a fairly irregular shape, which results in complexity in regards to producing reference systems by which to reference our maps and data against it.

## Slide 7: Modeling the Earth
True Earth surface
Geoid (Includes ocean)
Ellipsoid
Earth Model
Notes: In order to model the Earth, simplification is required.
The true Earth surface need to be generalized. First, it is generalized to a geoid.
This is further simplified to an ellipsoid.
We will explore these concepts now.

## Slide 8
https://en.wikipedia.org/wiki/Geoid
Geoid: gravity-related vertical reference
In geodesy, the geoid is an imaginary sea (mean sea level) that covers the entire Earth
It is not affected by wind, waves, the Moon, or forces other than Earth’s gravity. .
Notes: The geoid models the distribution of mass across the Earth, which is not uniform. The Earth is a bumpy surface.
This is partially accomplished by measuring gravitational forces across the globe.
A conceptualization of the geoid is a globe that is fully covered by water or has no continental masses.
Because there are differences in mass and gravitational forces across the globe, the water surface would not be smooth.
Instead, it would be a smoothly undulating shape.
This smoothly undulating shape that takes into account the distribution of mass is called the geoid.
The geoid surface can them be used as a reference for zero elevation.

## Slide 9
Geoid Height

## Slide 10: Geoid height

## Slide 11: What Do We Really Mean by 'Sea Level'? A Journey into the Geoid

## Slide 12
We need a mathematically simple model of the Earth’s Surface
We use an ellipsoid / spheroid
There are different ellipsoids/ spheroids used
Combined with ground survey data, we call these datums
Datum
Notes: The geoid is still a complex shape that cannot be modeled with a simple mathematical equation.
So, it is further simplified to an ellipsoid or spheroid model of the Earth.
This is a mathematical model that approximates the geoid as a smooth surface. Basically, this is a 3D ellipse.
Combining this model with ground survey data allows us to produce datums.
These datums serve as the reference systems by which we represent locations on Earth’s surface.
Our map and geospatial data will be referenced to one of these models.
The arc lengths may be measured by surface surveys, and the angles from astronomical observations

## Slide 13: What is datum?

## Slide 14: Horizontal datum
A mathematical model and reference system
It defines how to pinpoint locations on the Earth's surface using latitude and longitude coordinates

## Slide 15: The World at Zero: Equator & Prime Meridian
                Using Google Earth, find the location at the intersection of the Equator (0° latitude) and the Prime Meridian (0° longitude). Does this point fall on land or in the ocean?
Identify one country that lies near the Prime Meridian (0° longitude).
Identify one country that lies near the Equator (0° latitude).
* Click view – show gridlines to display gridlines on earth

## Slide 16: Vertical datum
A standardized reference surface used to define elevations and depths on the Earth's surface, serving as a "zero" point for measurements.

## Slide 17: Vertical datum - examples
Elevation of cities and landmarks 🏔️
– Example: The elevation of Denver (“Mile High City”) is measured relative to NAVD88 in the U.S.
Flood levels & floodplain mapping 🌊
– FEMA flood maps use vertical datums (e.g., NAVD88) to define the Base Flood Elevation (BFE).

## Slide 18
Relationship between terrain, an datum, and an ellipsoid
Notes: NGS (National Geodetic Survey),Triangulation survey
For the most of the past 150 years, the most accurate observations were referenced to the Sun, stars, or other celestial bodies
Every few years

## Slide 19
NGVD29: National Geodetic Vertical Datum of 1929
  No geoid, mean sea level
NAVD88: North American Vertical Datum of 1988 (NAVD88)
  GEOID03, GEOID09, GEOID12B
Common vertical datum
Notes: Example vertical datums in North America include the National Geodetic Vertical Datum of 1929 (NGVD29) and the more recent North American Vertical Datum of 1988 (NAVD88).
As technologies advance, updated versions of horizontal and vertical datums will be released.
GEOID18 is intended for use with coordinates in the North American Datum of 1983 (2011) [NAD 83 (2011) epoch 2010.00]. It provides orthometric heights consistent with the North American Vertical Datum of 1988 (NAVD 88), the Puerto Rico Vertical Datum of 2002 (PRVD02), or the Virgin Islands Vertical Datum of 2009 (VIVD09).

## Slide 20
Common Horizontal Datum
NAD27: North American Datum of 1927
NAD83: North American Datum of 1983
  NAD83(xx), xx represents year, version of datum adjustment
  NAD83(HARN/HPGN): High Accuracy Reference Networks or High Precision Geodetic Networks
WGS84: World Geodetic System 0f 1984
  WGS84(xx)
ITRF: International Terrestrial Reference Frames
  ITRF89, ITRF90, ITRF91
Notes: There are different datums by which we reference are horizontal measurements or coordinates on the Earth.
Examples include the North American Datum of 1927 (or NAD27), the North American Datum of 1983 (or NAD83), and the World Geodetic System of 1984 (or WGS83).
In North America, it is common to reference data against NAD83 or WGS84.
Global Navigation Satellite Systems, or GNSS, often make use of WGS84 as a worldwide datum.
Again, think of these as different models of the Earth, all of which are simplifications.
The HARN and subsequent NAD83 adjustments are largely satellite-based, including WGS84 and ITRF

## Slide 21
Datum
WGS84 and ITRF can be considered equivalent for most purpose, as difference between them since 1995 are generally only a few centimetres
Bolstad, 2019
Notes: Tectonic movement, crustal deformation

## Slide 22
Datum Inconsistent

## Slide 23: Which datum google map use?

## Slide 24
Datum Pairing
Pairing for horizontal and vertical datums for North America
Notes: Example vertical datums in North America include the National Geodetic Vertical Datum of 1929 (NGVD29) and the more recent North American Vertical Datum of 1988 (NAVD88).
As technologies advance, updated versions of horizontal and vertical datums will be released.
GEOID18 is intended for use with coordinates in the North American Datum of 1983 (2011) [NAD 83 (2011) epoch 2010.00]. It provides orthometric heights consistent with the North American Vertical Datum of 1988 (NAVD 88), the Puerto Rico Vertical Datum of 2002 (PRVD02), or the Virgin Islands Vertical Datum of 2009 (VIVD09).

## Slide 25
Coordinates on a Sphere
  Latitude and Longitude
  Specified as angles or degrees
  Latitude: Angles from equator
    Range 0-90 N/S
  Longitude: Angles from prime meridian
    Range 0-180 E/W
Geographic Coordinate Systems
© 2013 by John Wiley & Sons, Inc. All rights reserved.
Notes: Coordinates on Earth are measured in degree units relative to the center of the Earth.
Latitude is measures as an angle of rise relative to the center of the Earth while longitude represents angles of rotation around the center of the Earth.
Note that it is not easy to make measures of distance using lengths on a spherical surface.

## Slide 26
Geographic Coordinate Systems
Latitude (Parallels):
  Measures north to south
  90° in each hemisphere
  Increases as you go north in the northern hemisphere
  Increases as you go south in the southern hemisphere
  Zero in Equator
https://commons.wikimedia.org/wiki/File:Latitude_and_Longitude_of_the_Earth.svg
Notes: Latitude measures north to south or up and down. There are 90° of latitude in each hemisphere. The value increases as you move north or south relative to the equator. The equator has a latitude of 0° and the poles have a latitude of 90°.

## Slide 27
Geographic Coordinate Systems
Longitude (Meridians)
  Measures east to west
  180° in each hemisphere
  Increases as you go east in the eastern hemisphere
  Increases as you go west in the western hemisphere
  Zero is Prime Meridian, going through Greenwich, England
https://commons.wikimedia.org/wiki/File:Latitude_and_Longitude_of_the_Earth.svg
Notes: Longitude measures east to west or side to side. There are 180° of longitude in each hemisphere, east and west. Longitude increases has you move west in the western hemisphere and increase as you move east in the eastern hemisphere. 0° longitude is refined relative to the prime meridian which passes through Greenwich, England.
It makes sense to use the equator to represent 0° latitude. The 0° reference for longitude is somewhat arbitrary.
We can specify the northern or southern hemispheres for latitude by including an “N” or “S” with the measurements. For longitude, we can use “E” or “W”.
In software, this can be problematic due to the mix of numbers and letters. So, instead we tend to use positive angles to represent the northern or eastern hemispheres and negative angles to represent the southern or western hemispheres.
Coordinates referenced to a datum representing the 3D Earth or globe are known as geographic coordinate systems as opposed to projected coordinate systems, which will be discussed later.

## Slide 28
1 Degree = 60 Minutes = 3600 Seconds
  ˚ = Degrees
  ‘ = Minutes
  “ = Seconds
  1.5 ˚ =1 ˚ 0.5X60’= 1 ˚ 30’
  1 ˚ 30’ = 1° + (30’/60’) = 1.5°
Geographic Coordinate Systems
Notes: One degree of latitude or longitude can be a large distance. So, in order to provide precise measurements, we need to be able to further divide degrees into smaller units.
A degree can be divided into minutes and second, similar to an hour on a clock.
1 degree equals 60 minutes or 3600 seconds.
We can also use decimal degrees as opposed to minutes and seconds.
It is possible to convert between degrees, minutes, and second and degrees and decimal degrees.

## Slide 29
Advantages:
  Accurate representation
  Latitude and longitude lines
  Without distortion
  Disadvantages
    Expensive to make
    Cumbersome to handle and store
    Difficult to measure distance
    Not fully visible at one view
Geographic Coordinate Systems
Image from Google Earth
Notes: There are some advantages to modeling the Earth as a 3D globe. First, this is an accurate representation in which map features and latitude and longitude lines can be plotted without distortion.
However, there are some disadvantages. Making globes can be expensive. They are also cumbersome to handle and store. It is also not easy to make distance measurements on the curved surface of the globe. Duo to the 3D nature of a globe, it is not possible to view the entirety of Earth’s surface from a single vantage point.
So, we need a means by which to represent the curved, 3D Earth in a flat map space. We do this using projections, which we will discuss next.

## Slide 30
Map projections allow us to view the 3D Earth on a 2D surface
  Earth is mathematically projected to a surface that can be made flat
  We now make measurements in distance or length units as opposed to degrees
Projected Coordinate Systems
https://commons.wikimedia.org/wiki/File:Cartesian_coordinate_system_(comma).svg
Notes: Instead of using a the 3D spherical globe, we can mathematically transform the Earth into a flat map space.
Now, instead of making measurements of distance or length in angles, we can make measurements in length units.
These 2D surfaces are known as projected coordinate systems or map projections.
They allow us to make measurements in a Cartesian coordinate system on a plane.

## Slide 31
  They allow us to make measurements in a Cartesian coordinate system on a plane
  These 2D surface are known as map projections.
Projected Coordinate Systems
https://commons.wikimedia.org/wiki/File:Cartesian_coordinate_system_(comma).svg

## Slide 32: Geographic vs Projected Coordinate Systems
Image from ArcGIS API for JavaScript
Image from ArcGIS API for JavaScript
Notes: This slide provides an example of the difference between geographic and projected coordinate systems.
The globe provides a 3D representation of the Earth where measurements are made in angles.
In contrast, projections are 2D and allow for measurements to be made in Cartesian coordinate space.

## Slide 33
Datum/Projection Info in ArcGIS
Notes: Datum and sometimes projection information are associated with maps and geospatial data layers.
In ArcGIS Pro, datum and projection information for a layer can be found in the Source tab.
We will talk about projections later in this module.

## Slide 34
Datum
Transformation
  Converting coordinates from one datum to another
    Shift origin
    Scale
    rotation
Bolstad, 2019

## Slide 35: MAP PROJECTION
Conversion from geographic to projected coordinates
Bolstad, 2019

## Slide 36
Developable Surfaces
  Geometric surface that can be flattened
Cylindrical Projections = Cylinder Conic Projections = Cone Azimuthal Projections = Plane
Map projection
Notes: In order to flatten the Earth, coordinates on the globe must be mathematically transformed or moved to a geometric surface that can be flattened. These are called developable surfaces.
The most commonly used surfaces are cylinders, cones, and planes. Cylindrical projections use cylinders, conic projections use cones, and azimuthal projections use planes.
There are other shapes available or shapes can be combined. Here, we will focus on just these most commonly used surfaces.
Note that all three of these surface can be flattened. If you cut a cylinder, it can be folded out to a plane. A cone can be folded out into a fan shape.

## Slide 37
Developable Surfaces
  Geometric surface that can be flattened
Map projection
Bolstad, 2019

## Slide 38
Cylindrical Projection
This creates a rectangular grid
Distortion increases toward the poles — shapes and areas get stretched
Good for navigation
* Creation of cylindrical projection

## Slide 39
Plane projection
Plane positioned at pole
Grid:
  Longitude: straight, radiating
  Latitude: circles
Distortion increases away from center ("principal point")
Good for polar regions
Can't show more than half the world.
Plane projection

## Slide 40
Conic projection
Hold cone over pole
Grid:
  Longitude: straight, converge
  Latitude: curve
  Distortion increases away from standard parallel
Good for Mid-latitudes
Conic projection

## Slide 41
All map projections produce distortions of at least one of the following:
  Shape
  Area
  Distance
  Direction
Shape
Area
Distance
Direction
3D Earth
2D Map
Map projection
Notes: Since the curved, 3D surface of the Earth is converted to a flat space, some distortions will be produced.
It is not possible to convert a curved 3D surface into a flat surface without some distortions.
Specifically, map projections can produce distortions in feature shape, relative area of features, distance between features, and direction between locations.
The type and magnitude of the distortions produced depends on the projection used.

## Slide 42
All map projections produce distortions of at least one of the following:
  Shape
  Area
  Distance
  Direction
Map projection
Bolstad, 2019
Mercator
Transverse Mercator

## Slide 43
Map projection
Why all world maps are wrong?

## Slide 44
Type
Conformal Projections: preserves local angles and shape
Equivalent Projections: represents areas in correct relative size
Equidistant Projections: maintains consistent scale or distance along certain lines
Azimuthal Projections: maintains certain accurate directions relative to certain vantage point
Conformal and equivalent projections’ properties are mutually exclusive
Conformal and equivalent projections’ properties are global properties
Equidistant and azimuthal projections’ properties are local properties and may be true only from or to the center of the map projection
Map projection
Notes: Four broad types of projections exist based on what map properties are maintained.
Conformal projections maintain local angles and shapes. Equivalent projections maintain areas of features in correct relative size. Both are global properties, or shape or size can be maintained across the entire globe not just for specific areas. Also, these properties are mutually exclusive. Or, you cannot maintain both shape and relative size.
Equidistant projections maintain scale or distance along certain lines while azimuthal projections maintain accurate directions relative to a certain vantage point. Equidistant and azimuthal properties are local properties and may be true only from or to the center of the map projection. You cannot maintain distance or direction between all points in the map space.

## Slide 45
  Cylindrical conformal projection
  Parallels and meridians cross at right-angles
World projection - Mercator
Tissot Indicatrix
Distort size but not shape
  Without any distortions, the circles will all be the same shape and size
Q: In the projection, are the circles distorted in shape or in size?
🤔
Notes: Mercator projections are examples of cylindrical projections that are conformal, or maintain shape and local angles. (To preserve individual angles describing the spatial relationships, a Conformal projection must show the perpendicular graticule lines intersecting at 90-degree angles on the map)
Relative size tends to be heavily distorted. For example, the Tissot Indicatrix suggests that sizes close to the poles are much larger than they should be in comparison to equatorial features. Remember from the example above that Greenland is actually smaller than Australia.
In Mercator projections, parallels and meridians will cross at right-angles.

## Slide 46
  Modification of Mercator projection that is commonly used for web maps
  Bing Maps, OpenStreetMap, Google Maps, MapQuest, ArcGIS Online
Map projection – Web Mercator
http://cartonerd.blogspot.com/2014/08/web-mercator-and-comparisons.html
Notes: Web Mercator is a modification of the Mercator projection that is commonly used in web maps including Bing Maps, OpenStreetMap, Google Maps, MapQuest, and ArcGIS Online.
It uses a true sphere as opposed to a spheroid.
One reason this projection is used on the web is that it is easy to generate tiles from data since latitude and longitude lines intersect at right angles.

## Slide 47
  Equivalent projection
  Pseudo cylindrical
  Not based on developable surface
Map projection - Mollweide
Distort shape but not size
Q: In the projection, are the circles distorted in shape or in size?
🤔
Notes: Mollweide is an example of a equivalent projection that maintains relative size or area but distorts shape and local angles.
It is pseudosylindrical, which means that is uses multiple cylinders as opposed to one in an attempt to further minimize distortions.

## Slide 48
Class Activity
Explore the true size tool https://thetruesize.com/#.
  Does Greenland look larger or smaller than Brazil on the basemap?
  Search for ‘Greenland’
  Drag Greenland over Brazil to compare their areas

## Slide 49
Not Projected
Mercator
US projections
Map projection
Notes: We will now discuss continental-scale projections using the United States as an example.
The first image shows the US as not projected. Or, latitude and longitude are being treated like Cartesian coordinates in flat space. This results in some extreme distortions and should be avoided.
The second image shows a Mercator projection for the US. Here, shape and local angle is maintained but relative size is distorted.

## Slide 50
Albers Equal Area
Lambert Conformal Conic
US projections
Map projection
Notes: When creating maps of the US, I prefer to use Albers Equal Area or Lambert Conformal Conic.

## Slide 51
US projections: Albers Equal Area
  Conic
  Equivalent
  Maintains area
  Distort shape and local angles
Map projection
Notes: Albers Equal Area uses a conic developable surface with two standard parallels. It is equivalent, so it maintains relative size but distorts shape and local angles.
However, distortions are generally pretty minimal.

## Slide 52
US projections: Lambert Conformal Conic
  Conic
  Conformal
  Maintains shape and local angles
  Distorts local size
Map projection
Notes: Lambert Conformal Conic also uses a cone with two standard parallels. Since it is conformal it maintains shape and local angles but distorts local size.
However, distortions are minimal.
So, if I want to created a map of the US that maintains relative size, I tend to use Albers Equal Area. If I want to maintain shape, I will use Lambert Conformal Conic.

## Slide 53: Example Scenarios
An airline wants to create flight maps across the contiguous U.S.
The U.S. Census Bureau makes a map of population density by state.
Q: Which projection we should use in above scenario?
🤔

## Slide 54
Examples
  Projected coordinate systems do not use longitude and latitude to measure locations
  Instead, they use map units of the projection itself:
  Meters (UTM, Albers, most others)
  Feet (State Plane, few others)
Map projection

## Slide 55
Universal Transverse Mercator (UTM)
  60 zones
  Location provided in meters as Easting and Northing
  Northing: meters north of equator
    In northern hemisphere, equator is assigned a value of 0 meters, add as you go up
    In southern hemisphere, equator is assigned a value of 10,000,000 meters, subtract as you go down
  Easting: distance from central meridian in UTM zone
    Central meridian is assigned a value of 500,000 meters
    Add as you go east
    Subtract as you go west
Map projection
Notes: We will now discuss projections that are appropriate at more local scales, such as for states, counties, or cities.
Universal Transverse Mercator is a set of projections that are commonly used at these scales.
This is not one system but a set of systems in which the Earth is broken into 60 zones.
Within each zone coordinates are provided in length units, generally meters, as northing and easting.
Northing measures up and down or north to south. In the northern hemisphere, the equator is assigned a value of 0 meters, and you add as you move north. So, this is effectively the distance from the equator. In the southern hemisphere, the equator is assigned a value of 10,000,000 meters, and you subtract as you move south.
Easting is calculated relative to the central meridian or center line in each zone. The central meridian is assigned a value of 500,000 meters, and you add as you move east of it and subtract if you move west.

## Slide 56
Universal Transverse Mercator (UTM)
Map projection
Bolstad, 2019
Notes: The UTM systems break the Earth into 60 zones vertically.
Each zone is only appropriate for areas within it. You should not project the entire Earth to a single UTM projection.
Easting values will be defined relative to the central meridian in each zone.
In the US, the zone number increases as you move east and decreases as you move west.
The majority of Arkansas is in UTM Zone 15 North. So, this is a common projection for Arkansas. So, Arkansas generally uses a geographic coordinate system of NAD83 or WGS84 and a projected coordinate system of UTM Zone 15 North.
Some states fit well into a single UTM zone, for example Nevada, Utah, and Alabama. Others do not, such as California or Pennsylvania.
For states that do not fit well into one UTM zone, other projections are generally used to display them.

## Slide 57
State Plane Coordinate System
  125 geographic zones designed for specific regions in the United States
  Zones follow county boundaries
  city- to county-scale
https://www.e-education.psu.edu/natureofgeoinfo/c2_p26.html
Map projection
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 58
State Plane Coordinate System
  Transverse Mercator projection (for states with long north-south axis)
  Lambert conformal conic projection (for states with long east-west axis)
Map projection
Lambert conformal conic
Transverse Mercator
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 59
State Plane Coordinate System
  The zones may change!
Map projection
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 60
It is not a coordinate system, but used widely for land parcels since 1800s
  Divided lands by north-south lines, 6 miles apart
  East-west lines were surveyed perpendicular to those north-south lines, also at 6 miles intervals
  30 states adopted PLSS
Public Land Survey System
Bolstad, 2019
Notes: For mapping smaller extents within states, state plane coordinate systems are commonly used.
It is common for surveyors to use these systems. Measurements are commonly made in feet or meters. Each coordinate system has a defined baseline, like northing and a false meridian, like easting, to which the coordinate measurements are referenced. Different projections are used depending on the specific coordinate system.
These systems allow for very accurate measurements and are commonly used at the city- to county-scale.
120 different zones generally follow county boundaries (except in Alaska). Larger states are divided into multiple zones, such as the “Colorado North Zone.” States with a long north-south axis (such as Idaho and Illinois) are usually mapped using a Transverse Mercator projection, while states with a long east-west axis (such as Washington and Pennsylvania) are usually mapped using a Lambert Conformal projection. In either case, the projection's central meridian is generally run down the approximate center of the zone.
SPCS 27 and SPCS 83
The boundaries of which usually follow county lines
States that are long in the east–west direction are typically divided into zones that are also long east–west. These zones use the Lambert conformal conic projection, because it is good at maintaining accuracy along an east–west axis, due to the projection cone intersecting the earth's surface along two lines of latitude. Zones that are long in the north–south direction use the Transverse Mercator projection because it is better at maintaining accuracy along a north–south axis, due to the circumference of the projection cylinder being oriented along a meridian of longitude.
125 (as of 2001). There are 110 zones in the contiguous US, with 10 more in Alaska, 5 in Hawaii, and one for Puerto Rico and US Virgin Islands.

## Slide 61
Place roads, powerlines, and other public services
Public Land Survey System
Bolstad, 2019
Notes: The PLSS is important because:
1) The PLSS lines are often property boundaries, they form natural corridors in which to place roads, powerlines, and other public services; they are often evident on the landscape. Many road intersections occur at PLSS corner points, and these can be viewed and referenced on many maps or imagery used for GIS database development efforts. Further, PLSS corners are sometimes resurveyed using high precision methods to provide property line control, particularly when a GIS is to be developed.

## Slide 62
Projection used is related to type of map and area covered by map (extent)
Continental-scale data (North America)
  Geographic projection (decimal degrees)
  Lambert Conformal Conic
  Albers Equal Area
State-scale data (Arkansas)
  UTM Projection, Zone 15N
  County, city-scale data
  State Plane
Map projection
Notes: The best map projection to use partially depends on the extent being mapped or the scale of the map.
We will now investigate some common map projections that can be used at different scales.
Note that all maps and spatial data layers will be referenced to a datum or geographic coordinate system.
If the map or data have been projected, they will also have a projected coordinate system where measurements are made in length units as opposed to angles.
We will begin with a discussion of some common global-scale projections followed by continent- and sate-scale options.

## Slide 63
Should use same projection and datum for all data
Use projection appropriate for scale and extent
Think about what map properties are maintained or distorted
Best Practice
Notes: This slide highlights best practices for working with projections.
First, it is generally best to use the same projection for all data layers in a map or project to avoid any issues with misalignment.
You should use a projection appropriate for the scale and extent of the map. For example, you would not use a specific UTM zone to project the entire globe. On the other hand, a global projection would not be the best choice for data just within Arkansas.
You should also think about what map properties are maintained or distorted. If you are interested in maintaining relative size, then you should use an equivalent projection.

## Slide 64
ArcGIS can apply a projection transformation on-the-fly
So, it is not always necessary to reproject data
Okay if you are visualizing the data
Need to reproject if you plan to perform an analysis
Projection-on-the-Fly (ArcGIS)
Notes: Note that ArcGIS Pro can apply a projection transformation on-the-fly or in memory.
So, data that are read into a map that are in a different projection than the map can be reprojected to match the map on-the-fly.
So, it is not always necessary to reproject data if you are simply visualizing it or making a map layout.
However, I suggest transforming all data layers into the same projection if you plan to perform spatial analysis.

## Slide 65
Thank you!